## Slide 1: A Case for Speculative Address Translation with Rapid Validation for GPUs
Junhyeok Park1 Osang Kwon1 Yongho Lee1
Seongwook Kim1 Gwangeun Byeon1 Jihun Yoon1 Prashant J. Nair2 Seokin Hong1
1
2

## Slide 2
Outline
1. Virtual Memory in GPUs – Challenges ☜
1
2. Avatar • Speculative address translation • Rapid Validation
3. Evaluation
4. Summary

## Slide 3
2
GPUs in Heterogeneous Platform
CPU Memory
~X TB
GPU Memory
~XX GB
GPU
GPU
CPU
HBM
GPU Memory
~XX GB
GDDR

## Slide 4
2
GPUs in Heterogeneous Platform
CPU Memory
~X TB
GPU Memory
~XX GB
GPU
CPU
HBM
GPU Memory
~XX GB
GPU
Unified Memory space
➊ Seamless data sharing ➋ Efficient memory management
GDDR
Virtual Memory
Virtual Memory

## Slide 5
Address Translation in GPUs
3
GPU
Shared
L2 TLB
L2 Cache
L1 Cache
L1 TLB
GPU Main Memory
GPU Core
Page walker
Page walker
Page walker
Page walker
L1 TLB
Shared
L2 TLB

## Slide 6
Memory Request
Address Translation Overhead
Address Translation in GPUs
L1 TLB •
L1 Cache
L2 TLB • Page Walk
Look up
L1 TLB miss
4
Shared L2 TLB
Page Walker
L1 TLB
L1 Cache
L2 Cache
GPU Main Memory
VIPT Cache
Miss
Miss
L2 TLB miss
GPU
Shared
L2 TLB
L2 Cache
L1 Cache
L1 TLB
GPU Main Memory
GPU Core
Page walker
Page walker
Page walker
Page walker
L1 TLB
Shared
L2 TLB

## Slide 7
VIPT Cache
Address Translation Overhead
Address Translation in GPUs
L1 TLB •
L1 Cache
L2 TLB • Page Walk
4
Shared L2 TLB
Page Walker
L1 TLB
L1 Cache
L2 Cache
GPU Main Memory
Miss
Miss
Memory Request
L1 TLB •
L1 Cache
L2 Cache • Memory
L1 TLB •
L1 Cache
Replay
TLB Hit!!
L1 Cache miss
Replay
Return
L2 Cache miss
Miss
Miss
GPU
Shared
L2 TLB
L2 Cache
L1 Cache
L1 TLB
GPU Main Memory
GPU Core
Page walker
Page walker
Page walker
Page walker
L1 TLB
Shared
L2 TLB
Look up
L1 TLB miss
L2 TLB miss

## Slide 8
Address Translation in GPUs
Memory access latency considering address translation overhead
5

## Slide 9
Address Translation in GPUs
Address translation (page walk) increase memory access latency up to 1.96x
5

## Slide 10
Address Translation in GPUs
Address translation (page walk) increase memory access latency up to 1.96x
5
Needs efficient address translation support for GPUs

## Slide 11
Outline
1. Virtual Memory in GPUs – Challenges
7
2. Avatar ☜ • Speculative address translation • Rapid Validation
3. Evaluation
4. Summary

## Slide 12
Avatar
8
Accelerated Virtual Address Translation with Address Speculation and Rapid Validation
Speculative Address Translation
Rapid Validation
for speculation
Return to GPU core
L1 TLB •
L1 Cache
L2 TLB • Page Walk
L1 TLB •
L1 Cache
L2 Cache • Memory
L1 TLB •
L1 Cache
Saved
L1 TLB •
L1 Cache
L2 Cache • Memory
L1 TLB •
L1 Cache
Our Goal

## Slide 13
Avatar
8
Accelerated Virtual Address Translation with Address Speculation and Rapid Validation
Speculative Address Translation
Rapid Validation
for speculation
Return to GPU core
L1 TLB •
L1 Cache
L2 TLB • Page Walk
L1 TLB •
L1 Cache
L2 Cache • Memory
L1 TLB •
L1 Cache
Saved
L1 TLB •
L1 Cache
L2 Cache • Memory
L1 TLB •
L1 Cache
Our Goal
➊ How to speculate?
➋ How to validate rapidly?

## Slide 14
Outline
1. Virtual Memory in GPUs – Challenges
9
2. Avatar • Speculative address translation ☜ • Rapid Validation
3. Evaluation
4. Summary

## Slide 15
Speculative Address Translation
10
How to speculate?
➋ Implementation: CAST
➊ Key Observation

## Slide 16
Speculative Address Translation
10
How to speculate?
➋ Implementation:
CAST
➊ Key Observation

## Slide 17
Key Observation – Page Contiguity
CPU memory
GPU memory
Memory Management in Unified Memory
Unified Memory space
Page 2
Page 1
GPU
CPU
11

## Slide 18
Key Observation – Page Contiguity
CPU memory
GPU memory
Memory Management in Unified Memory
Page fault
Unified Memory space
Page 2
Page 1
GPU
CPU
11

## Slide 19
Key Observation – Page Contiguity
CPU memory
GPU memory
Memory Management in Unified Memory
Page migration
Unified Memory space
GPU
CPU
11
Page 1
Page 2

## Slide 20
2MB virtual chunk
Virtual
address space
GPU physical
address space
2MB
physical chunk
2MB physical space
reserved
VPN 0x000
Key Observation – Page Contiguity
Leveraging 2MB page contiguity
VPN 0x1FF
PPN 0x100
VPN 0x2FF
Classify fault
by 2MB VA
12
Page 2
VPN 0x002
Page 1
VPN 0x001

## Slide 21
Virtual
address space
GPU physical
address space
2MB physical space
reserved
VPN 0x000
Page 1
Key Observation – Page Contiguity
Leveraging 2MB page contiguity
VPN 0x1FF
PPN 0x100
VPN 0x2FF
VPN 0x001
Classify fault
by 2MB VA
GPU page table
VPN 0x000 VPN 0x001 PPN 0x101
VPN 0x002 PPN 0x102
VPN 0x003
· · · ·
0x001
0x101
12
0x002
0x102
Page 2
VPN 0x002

## Slide 22
Key Observation – Page Contiguity
GPU page table
VPN 0x000 PPN 0x100 VPN 0x001 PPN 0x101
VPN 0x002 PPN 0x102
VPN 0x003
VPN 0x004 PPN 0x104
· · · ·
VA space
PA space
· · · ·
· · · ·
Page contiguity :
contiguous virtual addresses are mapped to contiguous physical addresses,
particularly within each 2MB region
13

## Slide 23
➊
➋
➋ - ➊ = 0x100
Exploiting Page Contiguity for Speculation
GPU page table
VPN 0x000 PPN 0x100 VPN 0x001 PPN 0x101
VPN 0x002 PPN 0x102
VPN 0x003
VPN 0x004 PPN 0x104
· · · ·
➊
➋
➋ - ➊ = 0x100
V2P Offset
Contiguous region maintains the same virtual-to-physical (V2P) offset
14

## Slide 24
· ·
Exploiting Page Contiguity for Speculation
GPU page table
VPN 0x000 PPN 0x100 VPN 0x001 PPN 0x101
VPN 0x002 PPN 0x102
VPN 0x003
VPN 0x004 PPN 0x104
VPN 0x103 PPN ???
➊
➋
➋ - ➊ = 0x100
V2P Offset
Contiguous region maintains the same virtual-to-physical (V2P) offset
14

## Slide 25
Speculates the PPN!!
· ·
Exploiting Page Contiguity for Speculation
GPU page table
VPN 0x000 PPN 0x100 VPN 0x001 PPN 0x101
VPN 0x002 PPN 0x102
VPN 0x003
VPN 0x004 PPN 0x104
VPN 0x103 PPN ???
➊
➋
➋ - ➊ = 0x100
V2P Offset
VPN + V2P Offset = PPN
0x103 + 0x100 = 0x203
Contiguous region maintains the same virtual-to-physical (V2P) offset
14

## Slide 26
Speculative Address Translation
15
How to speculate?
➋ Implementation:
CAST
➊ Key Observation

## Slide 27
Speculative Address Translation
15
How to speculate?
➋ Implementation:
CAST
➊ Key Observation

## Slide 28
➊ The same load instructions
likely touch a contiguous region
CAST: Contiguity-Aware Speculative Translation
GPU page table
VPN 0x000 PPN 0x100 VPN 0x001 PPN 0x101
VPN 0x002 PPN 0x102
VPN 0x003
VPN 0x004 PPN 0x104
VPN 0x1FF PPN 0x2FF
· ·
V2P Offset= 0x100
Request 1 (PC 0x01)
Request 2 (PC 0x01)
V2P Offset= 0x100
16

## Slide 29
CAST: Contiguity-Aware Speculative Translation
PC | State count | V2P Offset
0x03 |  | 
0x01 | 0 1 2 | 0x100
0x05 |  | 
Mapping Offset Detection Table
GPU page table
VPN 0x000 PPN 0x100 VPN 0x001 PPN 0x101
VPN 0x002 PPN 0x102
VPN 0x003
VPN 0x004 PPN 0x104
VPN 0x1FF PPN 0x2FF
· ·
V2P Offset= 0x100
Request 1 (PC 0x01)
Request 2 (PC 0x01)
V2P Offset= 0x100
➋ MOD table tracks V2P offset for each load instructions
16
➊ The same load instructions
likely touch a contiguous region

## Slide 30
Load Request
L1 TLB
L1 Cache
Miss
CAST: Contiguity-Aware Speculative Translation
17
CAST
MOD

## Slide 31
Load Request
L1 TLB
L1 Cache
Miss
TLB miss request
17
CAST: Contiguity-Aware Speculative Translation
CAST
MOD
+ .
PC | State count | V2P Offset
0x03 |  | 
0x01 | 2 | 0x100
0x05 |  | 
Mapping Offset Detection Table
≥threshold?
Speculated Physical Address
0x102 | 0x300
Speculated PPN
Page Offset
Enable
PC: 0x01 | 0x002 | 0x300
Page Offset
VPN

## Slide 32
Outline
1. Virtual Memory in GPUs – Challenges
18
2. Avatar • Speculative address translation • Rapid Validation ☜
3. Evaluation
4. Summary

## Slide 33
Rapid Validation
19
How to validate rapidly?
➋ Our Approach
• Key observation • Implementation:
CAVA
➊ Prior Approach • Lazy validation

## Slide 34
Rapid Validation
19
How to validate rapidly?
➋ Our Approach
• Key observation • Implementation:
CAVA
➊ Prior Approach • Lazy validation

## Slide 35
Limitation in Prior Approach
20
L2 TLB • Page Walk (Background)
Look up
L1 TLB miss
L1 Cache miss
L2 Cache • Memory
Speculative address translation
L1 TLB • L1 Cache
Lazy validation for speculative translation in CPUs

## Slide 36
Speculative Execution
Limitation in Prior Approach
L1 TLB • L1 Cache
L2 TLB • Page Walk (Background)
Look up
L1 Cache miss
L2 Cache • Memory
20
Normal Execution
Lazy validation for speculative translation in CPUs
Speculative address translation
L1 TLB miss
Validation – Correct Speculation

## Slide 37
Limitation in Prior Approach
L1 TLB • L1 Cache
L2 TLB • Page Walk (Background)
Look up
L1 Cache miss
L2 Cache • Memory
21
Validation – Incorrect Speculation
Speculative Execution
Normal Execution
Rollback
Speculative address translation
Limitation ➊: Expensive roll-back process
Penalty
L1 TLB miss

## Slide 38
Limitation in Prior Approach
L1 TLB • L1 Cache
L2 TLB • Page Walk (Background)
Look up
L1 Cache miss
L2 Cache • Memory
22
Validation – Incorrect Speculation
Speculative Execution
Normal Execution
Rollback
Speculative address translation
Limitation ➋: GPUs do not even support rollback mechanisms
L1 TLB miss

## Slide 39
Limitation in Prior Approach
L1 TLB • L1 Cache
L2 TLB • Page Walk (Background)
Look up
L1 Cache miss
L2 Cache • Memory
23
Validation
Execution
Speculative address translation
Simple Solution: To wait for validation to complete
L1 TLB miss
Waiting
Penalty

## Slide 40
Rapid Validation
24
➋ Our Approach
• Key observation • Implementation:
CAVA
➊ Prior Approach • Lazy validation
How to validate rapidly?

## Slide 41
Rapid Validation
24
➋ Our Approach
• Key observation • Implementation:
CAVA
➊ Prior Approach • Lazy validation
How to validate rapidly?

## Slide 42
Key Observation – Memory Compression
25
Compresses each 32-byte sector to 22 bytes (BPC Compression [Kim+, ISCA’16])
*sector: the basic data fetch unit in modern GPUs
On average, 67.5% of sectors can be compressed to 22 bytes

## Slide 43
CAVA: In-Cache Validation
Embedding page information within data for validation
26
Remaining region (10B)
Compressed data (22B)
Data (32B)

## Slide 44
CAVA: In-Cache Validation
Embedding page information within data for validation
26
Data (32B)
Compressed data (22B)
Page information
(VPN + Permissions)

## Slide 45
GPU
CAVA: In-Cache Validation
CPU
CPU Memory
GPU Memory
Memory Controller
GPU driver
Data page
Data page
Data page
Data page
27

## Slide 46
GPU
CAVA: In-Cache Validation
CPU
CPU Memory
GPU Memory
Memory Controller
GPU driver
Data page
Data page
Data page
Data page
Page information
The page information (VPN + permissions) is transferred with the data page
27

## Slide 47
GPU
CAVA: In-Cache Validation
CPU
CPU Memory
GPU Memory
Memory Controller
GPU driver
Data page
Data page
Data page
Page information
Data page
27
sector
Page information
Compressor
Compressed Sector

## Slide 48
GPU
GPU Memory
Memory Controller
Sector
CAVA: In-Cache Validation
CPU
CPU Memory
GPU driver
Data page
Data page
Data page
Page information
Data page
27
Page information
Compressor
Compressed Sector

## Slide 49
27
Page information
GPU
CAVA: In-Cache Validation
CPU
CPU Memory
GPU Memory
Memory Controller
GPU driver
Data page
Data page
Data page
Page information
Data page
Compressor
Compressed Sector
Sector
Signature (2B) | VPN + Permissions (8B) | Compressed data (22B)
Sector
Compression status distinction [Hong+, MICRO’18]
Sector
Sector

## Slide 50
CAVA: In-Cache Validation
Load Request
L1 TLB
L1 Cache
Miss
CAST
MOD
L2 TLB
Page Walker
L2 Cache
GPU Main Memory
Saved (➊ + ➋)
➊ Speculation with CAST
➊
➌ Address translation in the background
➌
28
➋
➋ Data fetched from the speculated address

## Slide 51
CAVA: In-Cache Validation
Load Request
L1 TLB
Miss
CAST
MOD
L2 TLB
Page Walker
L2 Cache
GPU Main Memory
L1 Cache
CAVA
29
Check whether sector is compressed
Compressed?
signature
C: a compression bit in each sector tag
C
Sector 0
C
Sector 1
C
Sector 2
C
Sector 3
L2 Cache Fill
GPU Memory
Sector
Sector
Sector
Sector

## Slide 52
Can be used
CAVA: In-Cache Validation
Load Request
L1 TLB
L1 Cache
Miss
CAST
MOD
L2 TLB
Page Walker
L2 Cache
GPU Main Memory
L1 Cache
CAVA
30
VPN: 0x002
Memory request information in MSHR
VPN | PPN | Sector
0x002 | 0x102 | 0
= .
L1 Cache
Data
Decompress
C
Sector 0
Fetch into L1 Cache

## Slide 53
Timeline Comparison
31
L1 TLB •
L1 Cache
L2 TLB • Page Walk
L1 TLB •
L1 Cache
L2 Cache • Memory
L1 TLB •
L1 Cache
Baseline
➊ Speculation + No Rapid Validation (CAST)
L2 TLB • Page Walk (Background)
L2 Cache • Memory
L1 TLB •
L1 Cache
Waiting
L1 TLB • L1 Cache
Saved

## Slide 54
Timeline Comparison
31
L1 TLB •
L1 Cache
L2 TLB • Page Walk
L1 TLB •
L1 Cache
L2 Cache • Memory
L1 TLB •
L1 Cache
Baseline
L2 TLB • Page Walk (Background)
L2 Cache • Memory
L1 TLB •
L1 Cache
➊ Speculation + No Rapid Validation (CAST)
L1 TLB • L1 Cache
L2 TLB • Page Walk (Background)
L2 Cache • Memory
L1 TLB •
L1 Cache
L1 TLB • L1 Cache
➋ Speculation + Rapid Validation (CAST + CAVA)
Saved
Saved
Waiting

## Slide 55
Outline
1. Virtual Memory in GPUs – Challenges
32
2. Avatar • Speculative address translation • Rapid Validation
3. Evaluation ☜
4. Summary

## Slide 56
Methodology
Simulator: GPGPU-Sim 4.0 [Khairy+, ISCA’20]
▶ Virtual memory support (Unified Memory / 4KB page for baseline)
Avatar Framework:
▶ 32-entry MOD table ▶ Data compression using the Bit-Plane Compression method [Kim+, ISCA’16]
Component | Parameter
L1 TLB | 32 entries (4KB), 16 entries* (2MB)
L2 TLB | 1024 entries (4KB), 128 entries* (2MB)
Page walk | 16 page walkers
* 2MB TLBs for page size promotion
33

## Slide 57
Methodology
Workloads: 20 applications from various benchmark suites
▶ Diverse data types ▶ Classified on TLB sensitivity
Comparison to Prior Works:
▶ Promotion [Ausavarungnirun+, MICRO’17]: Page size promotion ▶ CoLT [Pham+, MICRO’12]: Fixed-size TLB coalescing
▶ SnakeByte [Lee+, HPCA’23]: Multi-size TLB coalescing
34

## Slide 58
Evaluation
Speculation Accuracy - How many speculative translations are correct?
 90.3% Speculation Coverage - How many TLB misses are handled by CAST?
 74.3%
35

## Slide 59
Evaluation
Memory Access Latency Reduction Avatar - 44.5%↓
GPU Core Stall Cycles Reduction Avatar - 45.0%↓
36

## Slide 60
Evaluation
Performance Improvement Avatar - 37.2%↑ > Best of prior works - 27.1%↑
37
Chart: Normalized Performance
| LMD | FW | GEMM | SGEM | BP | MD | HIS | PAF | LUL | GC | FDT | BET | CON | CFD | SSSP | SPMV | CC | SC | KM | XSB | Gmean
Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Promotion | 1 | 1.013 | 1 | 1 | 1.0001 | 1.0916 | 1.2539 | 1.0143 | 1.0861 | 1.1046 | 1.1557 | 1.2351 | 1.09 | 1.3229 | 1.5317 | 1.7839 | 1.0103 | 1.1371 | 3.4765 | 1.4639 | 1.2224
CoLT | 1.0002 | 1.0183 | 1.0448 | 1.0853 | 1.0362 | 1.1297 | 1.2965 | 1.112 | 1.1802 | 1.1365 | 1.1759 | 1.2918 | 1.1089 | 1.3599 | 1.6013 | 1.8339 | 0.98913 | 1.2018 | 4.1995 | 1.5095 | 1.2718
SnakeByte | 0.99808 | 1.0064 | 0.94861 | 1.1596 | 1.1883 | 1.1252 | 1.1756 | 0.92389 | 1.0237 | 1.1159 | 1.1376 | 1.4721 | 1.3195 | 1.259 | 1.6405 | 1.6809 | 0.85109 | 1.1294 | 2.9152 | 1.3271 | 1.2188
Avatar | 1.0012 | 1.0163 | 1.1133 | 1.2464 | 1.0972 | 1.1433 | 1.3031 | 1.3265 | 1.1433 | 1.1873 | 1.2725 | 1.3541 | 1.3779 | 1.369 | 1.6749 | 1.9428 | 1.194 | 1.5093 | 3.7826 | 1.91 | 1.3725
TLB-insensitive
TLB-moderate
TLB-sensitive
3.47|4.19|2.91|3.78
37.2%

## Slide 61
Outline
1. Virtual Memory in GPUs – Challenges
38
2. Avatar • Speculative address translation • Rapid Validation
3. Evaluation
4. Summary ☜

## Slide 62
Summary
Problem: Address translation overhead in GPUs (34.5% slower compared to Ideal)
39

## Slide 63
Summary
Problem: Address translation overhead in GPUs (34.5% slower compared to Ideal)
Avatar: Speculative address translation overcoming GPUs’ architectural limit
▶ Speculative translation by exploiting page contiguity
▶ Rapid validation using page information embedded within data blocks
39

## Slide 64
Summary
Problem: Address translation overhead in GPUs (34.5% slower compared to Ideal)
Avatar: Speculative address translation overcoming GPUs’ architectural limit
▶ Speculative translation by exploiting page contiguity
▶ Rapid validation using page information embedded within data blocks
Avatar achieves an average speed up of 37.2% across various workloads
39

## Slide 65: A Case for Speculative Address Translation with Rapid Validation for GPUs
Junhyeok Park1 Osang Kwon1 Yongho Lee1
Seongwook Kim1 Gwangeun Byeon1 Jihun Yoon1 Prashant J. Nair2 Seokin Hong1
1
2
Thanks!

## Slide 66
Backup Slides
40
• Page Access Pattern of Load
• Without Rapid Validation
• Security Implications
• ML Workloads
• TLB Shootdown
• Workload Categorization

## Slide 67
Chart: Proportion
| LMD | FW | GEMM | SGEM | BP | MD | HIS | PAF | LUL | GC | FDT | BET | CON | CFD | SSSP | SPMV | CC | SC | KM | XSB | Gmean
Load locality | 1 | 1 | 1 | 0.99904 | 0.98072 | 0.8567 | 0.97205 | 0.95055 | 0.91752 | 0.93609 | 0.9747 | 0.96721 | 0.78011 | 0.97554 | 0.90116 | 0.89097 | 0.96987 | 0.70286 | 0.72255 | 0.51745 | 0.89026
Page Access Pattern of Load
89.0%
On average, 89.0% of memory accesses from the same instruction
fall within a 2MB memory chunk.
• Backup Slides

## Slide 68
Security Implications
C
Sector 0
G
C
Sector 0
G
C
Sector 0
G
C
Sector 0
G
Cacheline
Guarantee bit
Compression bit
Invisible
Validation
Incorrect
Correct
Can be used
Invalidates
the sector
• Backup Slides

## Slide 69
Without Rapid Validation
CAST-only (without rapid validation) achieves a 29.1% speedup.
29.1%
• Backup Slides

## Slide 70
TLB Shootdown
• Backup Slides
❶ Flush a page’s contents
from the caches
❷ Invalidate the PTE of
the page from the TLBs
(TLB shootdown)
❸ Transfer the page’s content to CPU (or other GPUs)
Time
❹ Zeroing the memory location where the migrated page was stored
(Invalidate all in-sector page information)
❺ Updates the page tables

## Slide 71
ML Workloads
Avatar outperforms the best prior work by 7.1% on average.
(a) Compressibility
(b) Performance
• Backup Slides

## Slide 72
Workload Categorization
• Backup Slides
Class | Benchmark | Abbr. | Data Type | Benchmark | Abbr. | Data Type
L | fw | FW | I | lavaMD | LMD | D
 | gemm | GEMM | F | sgemm | SGEM | F
M | backprop | BP | F | shoc-MD | MD | I
 | histogram | HIS | UI | pathfinder | PAF | I
H | lulesh | LUL | F | color-max | GC | I
 | fdtd2d | FDT | F | betweenness | BET | UI
 | convolution | CON | F | cfd | CFD | F
 | sssp | SSSP | I | spmv | SPMV | I/F
 | connected | CC | UI | s.cluster | SC | F
 | kmeans | KM | F | XSBench | XSB | I/D
* Denoted as I/UI/F/D for int/unsigned int/float/double