## Slide 1: Leveraging Chiplet-Locality for Efficient Memory Mapping in Multi-Chip Module GPUs
Junhyeok Park1, 2 Sungbin Jang2 Osang Kwon2 Yongho Lee2 Seokin Hong2
1ETRI 2Sungkynkwan University
58th IEEE/ACM International Symposium on Microarchitecture

## Slide 2
Outline
Background: Multi-Chip Module GPUs
1
Evaluation & Summary
Motivations & Goal
Chiplet-Locality Aware Page Placement

## Slide 3
Outline
Background: Multi-Chip Module GPUs
2
Evaluation & Summary
Motivations & Goal
Chiplet-Locality Aware Page Placement

## Slide 4
3
Scaling Monolithic GPU Designs
 | Tesla K40 (2013) | Tesla M40 | Tesla P100 | Tesla V100 | Ampere A100 | Hopper H100 (2022)
Compute Unit Count | 15 | 24 | 56 | 80 | 108 | 114
L2 Cache Size (MB) | 1.5 | 3 | 4 | 6 | 40 | 50
Chart: Compute Unit Count
| Tesla K40 | Tesla M40 | Tesla P100 | Tesla V100 | Ampere A100 | Hopper H100
SM Count | 15 | 24 | 56 | 80 | 108 | 114
Chart: 
| Tesla K40 | Tesla M40 | Tesla P100 | Tesla V100 | Ampere A100 | Hopper H100
L2 Cache Size (MB) | 1.5 | 3 | 4 | 6 | 40 | 50
GPU scaling trends in monolithic GPU designs (compute & memory)

## Slide 5
4
Scaling Monolithic GPU Designs
 | Tesla K40 | Tesla M40 | Tesla P100 | Tesla V100 | Ampere A100 | Hopper H100
GPU Die Size (mm2) | 551 | 601 | 610 | 815 | 826 | 814
Chart: 
| Tesla K40 | Tesla M40 | Tesla P100 | Tesla V100 | Ampere A100 | Hopper H100
GPU Die Size (mm^2) | 551 | 601 | 610 | 815 | 826 | 814
Chart: 
| 2004 | 2006 | 2008 | 2011 | 2014 | 2015 | 2017 | 2019 | 2020 | 2022 | 2025
Transistor Scaling (nm) | 90 | 65 | 40 | 28 | 20 | 16 | 10 | 7 | 5 | 3 | 2
Monolithic GPU scaling is becoming challenging!
  GPU die size plateaus
  Transistor scaling slows down
 | 2004 | 2006 | 2008 | 2011 | 2014 | 2015 | 2017 | 2019 | 2020 | 2022 | 2025
Transistor Scaling (nm) | 90 | 65 | 40 | 28 | 20 | 16 | 10 | 7 | 5 | 3 | 2

## Slide 6
Package
Package
5
Multi-Chip Module (MCM) GPUs
XBAR
GPU chiplet
XBAR
GPU chiplet
XBAR
GPU chiplet
DRAM
XBAR
GPU chiplet
DRAM
DRAM
DRAM
Monolithic GPU
DRAM
MCM
MCM designs enable continued scaling beyond monolithic designs

## Slide 7
6
Multi-Chip Module (MCM) GPUs
MCM-based GPU designs are already in use
AMD CDNA 4.0 MI350
GPU Chiplet
NVIDIA Blackwell Ultra GPU

## Slide 8
7
Multi-Chip Module (MCM) GPUs: Challenges
XBAR
XBAR
DRAM
DRAM
threads
data
GPU chiplet
GPU chiplet
Remote memory accesses occur when threads touch remotely mapped data
  Add latency and energy overhead

## Slide 9
8
Multi-Chip Module (MCM) GPUs: Challenges
XBAR
XBAR
DRAM
DRAM
threads
data
GPU chiplet
GPU chiplet
Remote
Access
Remote memory accesses occur when threads touch remotely mapped data
  Add latency and energy overhead
inter-chip interconnect

## Slide 10
Outline
Background: Multi-Chip Module GPUs
9
Evaluation & Summary
Motivations & Goal
Chiplet-Locality Aware Page Placement

## Slide 11
The Impact of Page Size
Virtual
Address Space
Physical
Address Space
4KB Page
4KB Page
4KB Page
4KB Page
4KB Frame
4KB Frame
4KB Frame
4KB Frame
. . . .
. . .
Using large pages is generally beneficial
(A) 4KB Pages
Entry 0
Entry 1
Entry 2
Entry 3
4KB-Page TLB
10

## Slide 12
11
The Impact of Page Size
Virtual
Address Space
Physical
Address Space
Virtual
Address Space
4KB Page
4KB Page
4KB Page
4KB Frame
4KB Frame
4KB Frame
4KB Frame
4KB Page
Physical
Address Space
64KB Page
. . . .
. . .
64KB Frame
Using large pages is generally beneficial
(B) 64KB Page
(A) 4KB Pages
Contiguous 
Contiguous 
Entry 0
Entry 1
Entry 2
Entry 3
4KB-Page TLB
Entry 0
64KB-Page TLB

## Slide 13
12
Larger Pages Can Hurt Performance
XBAR
XBAR
DRAM
DRAM
threads-0
threads-1
GPU chiplet
GPU chiplet
Data Structure A
size: 8KB
Chiplet-0
Chiplet-1
Example: memory mapping with small pages (e.g., 4KB)

## Slide 14
size: 8KB
13
Larger Pages Can Hurt Performance
page 1
Data Structure A
page 0
XBAR
XBAR
DRAM
DRAM
threads-0
threads-1
GPU chiplet
GPU chiplet
Chiplet-0
Chiplet-1
Example: memory mapping with small pages (e.g., 4KB)

## Slide 15
size: 8KB
14
Larger Pages Can Hurt Performance
Data Structure A
XBAR
XBAR
DRAM
DRAM
threads-0
threads-1
GPU chiplet
GPU chiplet
Chiplet-0
Chiplet-1
Example: memory mapping with small pages (e.g., 4KB)
page 1
page 0
Local Access
Local Access

## Slide 16
size: 8KB
15
Larger Pages Can Hurt Performance
page 1
Data Structure A
page 0
XBAR
XBAR
DRAM
DRAM
threads-0
threads-1
GPU chiplet
GPU chiplet
Chiplet-0
Chiplet-1
Example: memory mapping with large pages (e.g., 8KB)

## Slide 17
size: 8KB
16
Larger Pages Can Hurt Performance
Data Structure A
page 0’
XBAR
XBAR
DRAM
DRAM
threads-0
threads-1
GPU chiplet
GPU chiplet
Chiplet-0
Chiplet-1
Example: memory mapping with large pages (e.g., 8KB)

## Slide 18
size: 8KB
17
Larger Pages Can Hurt Performance
Data Structure A
XBAR
XBAR
DRAM
DRAM
threads-0
threads-1
GPU chiplet
GPU chiplet
Chiplet-0
Chiplet-1
Example: memory mapping with large pages (e.g., 8KB)
page 0’
Local Access
Remote
Access

## Slide 19
18
The Impact of Page Size in MCM Designs
Small Pages - Pros : Enable fine-grained page placement - Cons: Lower address-translation efficiency
Large Pages - Pros : Higher address-translation efficiency - Cons: Enforce coarse-grained page placement

## Slide 20
19
The Impact of Page Size in MCM Designs
Bars: Performance
Lines: Remote ratio
Performance across different page sizes

## Slide 21
20
The Impact of Page Size in MCM Designs
Higher remote ratio
Lower performance
Performance across different page sizes

## Slide 22
21
The Impact of Page Size in MCM Designs
Constant remote ratio
Higher performance
Performance across different page sizes

## Slide 23
22
The Impact of Page Size in MCM Designs
First Motivation: Each application exhibits different sensitivity to page size changes

## Slide 24
23
Chiplet-Locality in GPU Workloads
Second Motivation: Chiplet-Locality - A certain number of virtually contiguous pages are primarily used by the same chiplet
Page 0
Page 1
Page 2
Page 3
Virtual
Address Space
Contiguous 
threads-1
Chiplet-1
Chiplet-0
threads-0
Page 4
Page 5
Page 6
Page 7

## Slide 25
24
Chiplet-Locality in GPU Workloads
Proportion of the address range exhibiting chiplet-locality
- Chiplet-locality is a prevalent property of GPU workloads
- Arising from the intrinsic characteristics (parallelism) of GPU workloads
93.5%

## Slide 26
25
Our Goal
What: Provide the suitable page size (mapping size) for each application, with support for multiple sizes (Motivation 1)
How: Leverage chiplet-locality, which captures the access patterns of GPU workloads (Motivation 2)

## Slide 27
Outline
Background: Multi-Chip Module GPUs
26
Evaluation & Summary
Motivation & Our Goal
Chiplet-Locality Aware Page Placement

## Slide 28
27
Chiplet-Locality Aware Page Placement (CLAP)
What CLAP does
VPN 0x100 | PFN 0x000
VPN 0x101 | PFN 0x005
VPN 0x102 | PFN 0x009
GPU page table
VPN 0x103 | PFN 0x003
VPN 0x104 | PFN 0x103
VPN 0x105 | PFN 0x101
VPN 0x106 | PFN 0x107
VPN 0x107 | PFN 0x104
chiplet-0
chiplet-1
. . . .
1. Small Pages
VPN 0x100 | PFN 0x000
GPU page table
chiplet-0
. . . .
2. Large Pages
Remote
VPN 0x100 | PFN 0x000
VPN 0x101 | PFN 0x001
VPN 0x102 | PFN 0x002
. . . .
GPU page table
VPN 0x103 | PFN 0x003
VPN 0x104 | PFN 0x104
VPN 0x105 | PFN 0x105
VPN 0x106 | PFN 0x106
VPN 0x107 | PFN 0x107
chiplet-0
chiplet-1
. . . .
3. CLAP
Entry 0
Entry 1
Entry 2
Entry 3
Entry 4
Entry 5
Entry 6
Entry 7
TLB entries

## Slide 29
Chiplet-Locality Aware Page Placement (CLAP)
What CLAP does
VPN 0x100 | PFN 0x000
VPN 0x101 | PFN 0x005
VPN 0x102 | PFN 0x009
GPU page table
VPN 0x103 | PFN 0x003
VPN 0x104 | PFN 0x103
VPN 0x105 | PFN 0x101
VPN 0x106 | PFN 0x107
VPN 0x107 | PFN 0x104
chiplet-0
chiplet-1
. . . .
1. Small Pages
VPN 0x100 | PFN 0x000
GPU page table
chiplet-0
. . . .
2. Large Pages
Remote
VPN 0x100 | PFN 0x000
VPN 0x101 | PFN 0x001
VPN 0x102 | PFN 0x002
. . . .
GPU page table
VPN 0x103 | PFN 0x003
VPN 0x104 | PFN 0x104
VPN 0x105 | PFN 0x105
VPN 0x106 | PFN 0x106
VPN 0x107 | PFN 0x107
chiplet-0
chiplet-1
. . . .
3. CLAP
Entry 0
Entry 1
Entry 2
Entry 3
Entry 4
Entry 5
Entry 6
Entry 7
TLB entries
28
Entry 0
TLB entries

## Slide 30
Chiplet-Locality Aware Page Placement (CLAP)
What CLAP does
VPN 0x100 | PFN 0x000
VPN 0x101 | PFN 0x005
VPN 0x102 | PFN 0x009
GPU page table
VPN 0x103 | PFN 0x003
VPN 0x104 | PFN 0x103
VPN 0x105 | PFN 0x101
VPN 0x106 | PFN 0x107
VPN 0x107 | PFN 0x104
chiplet-0
chiplet-1
. . . .
1. Small Pages
VPN 0x100 | PFN 0x000
GPU page table
chiplet-0
. . . .
2. Large Pages
Remote
VPN 0x100 | PFN 0x000
VPN 0x101 | PFN 0x001
VPN 0x102 | PFN 0x002
GPU page table
VPN 0x103 | PFN 0x003
VPN 0x104 | PFN 0x104
VPN 0x105 | PFN 0x105
VPN 0x106 | PFN 0x106
VPN 0x107 | PFN 0x107
chiplet-0
chiplet-1
. . . .
3. CLAP
Entry 0
Entry 1
Entry 2
Entry 3
Entry 4
Entry 5
Entry 6
Entry 7
TLB entries
29
Entry 0
TLB entries
Reserved
Reserved
Chiplet-Locality
Entry 0-3
Merged TLB entries
Entry 4-7

## Slide 31
30
Chiplet-Locality Aware Page Placement (CLAP)
Application Execution Time
1.1. Chiplet-locality Sampling
1.2. Mapping Size Selection
1. Profiling Phase
CLAP’s process
2. Applying the selected size
Launch

## Slide 32
31
Profiling Phase
XBAR
XBAR
XBAR
XBAR
GPU chiplet
GPU chiplet
GPU chiplet
GPU chiplet
A portion of data pages (20%)
Gathering chiplet-locality samples
- With small pages, mapping each page into its desired chiplet, on demand

## Slide 33
32
Profiling Phase
Gathering chiplet-locality samples
- With small pages, mapping each page into its desired chiplet, on demand
A portion of data pages (20%)
XBAR
XBAR
XBAR
XBAR
GPU chiplet
GPU chiplet
GPU chiplet
GPU chiplet
pages 0-3
pages 4-7
pages 8-11
pages 12-15
Will follow
a similar pattern

## Slide 34
33
Profiling Phase
Tracking remote memory accesses to verify the samples - Taking the shared behavior into account when selecting the page size
XBAR
XBAR
XBAR
XBAR
GPU chiplet
GPU chiplet
threads-0
threads-1
page
Shared by multiple threads

## Slide 35
34
Profiling Phase
Selecting the suitable page size based on the samples - When the remote access ratio = 0 (not shared)
- Selecting the largest page size that still preserves data locality (= the size of chiplet-locality)
VPN 0x100 | PFN 0x000
VPN 0x101 | PFN 0x001
VPN 0x102 | PFN 0x002
VPN 0x103 | PFN 0x003
VPN 0x104 | PFN 0x104
VPN 0x105 | PFN 0x105
VPN 0x106 | PFN 0x106
VPN 0x107 | PFN 0x107
. . . .
chiplet-0
chiplet-1
GPU page table (mapped during the profiling phase)
4 contiguous pages
 Chiplet-locality
Suitable Page Size : 256KB
64KB mapping

## Slide 36
35
Profiling Phase
Selecting the suitable page size based on the samples - When the remote access ratio ≠ 0 (shared)
- Selecting a larger page than the chiplet-locality size
XBAR
XBAR
XBAR
XBAR
GPU chiplet
GPU chiplet
threads-0
threads-1
page
Shared by multiple threads
Remote accesses are
unavoidable

## Slide 37
36
Profiling Phase
Selecting the suitable page size based on the samples - When the remote access ratio ≠ 0 (shared)
- Selecting a larger page than the chiplet-locality size
VPN 0x100 | PFN 0x000
VPN 0x101 | PFN 0x001
VPN 0x102 | PFN 0x002
VPN 0x103 | PFN 0x003
VPN 0x104 | PFN 0x104
VPN 0x105 | PFN 0x105
VPN 0x106 | PFN 0x106
VPN 0x107 | PFN 0x107
. . . .
chiplet-0
chiplet-1
GPU page table (mapped during the profiling phase)
Suitable Page Size : 512KB
At least provide
efficient translation
64KB mapping

## Slide 38
256KB
physical frame
Reserved
37
Applying the Selected Size
Leveraging reservation-based mapping to form a large-page-like region
- The case where the selected size is 256KB
- Support diverse sizes that are power of two
Physical Address Space
(chiplet-0)
256KB frame
64KB
Virtual Address Space
64KB
64KB
64KB
256KB virtual address

## Slide 39
38
Cooperation with TLB Coalescing
Coalescing contiguously mapped pages
- Extending the TLB reach and allowing to fully benefit from the contiguously mapped region
VPN 0x100 | PFN 0x000
VPN 0x101 | PFN 0x001
VPN 0x102 | PFN 0x002
VPN 0x103 | PFN 0x003
VPN 0x100 | PFN 0x000
Contiguous 
Contiguous 
VPN 0x101 | PFN 0x001
VPN 0x102 | PFN 0x002
VPN 0x103 | PFN 0x003
VPN 0x100 | PFN 0x000 + offset 0x000 ~ 0x003
Base + Offset form
coalescing
TLB entries
GPU page table

## Slide 40
Outline
Background: Multi-Chip Module GPUs
39
Evaluation & Summary
Motivation & Our Goal
Chiplet-Locality Aware Page Placement

## Slide 41
Evaluation Environment
40
Simulator: GPGPU-Sim extended to model a 4-chiplet MCM design
Benchmarks: Conventional GPGPU workloads + GEMM operations with varying shapes
Prior Works for Performance Comparison:
Class | Techniques | Characteristics
Group A | Static 64KB & 2MB paging; | - Mapping with conventional page sizes
Group B | GRIT [HPCA’24]; MGvm [MICRO’22]; Barre [ISCA’24] | - Address NUMA issues in multi GPU domains
Group C | C-NUMA [ASPLOS’13, ATC’14] C-NUMA with multiple page size support | - Address NUMA issues in NUMA-CPU systems

## Slide 42
Performance
41
IPC Comparison
- CLAP improves performance by up to 19.2% compared to prior works
Class | Consideration |  | 
 | A: Address Translation (Page Size) | B: Remote Accesses | C: Impact of Page Size
Group A | √ or X | X or √ | X
Group B | √ or X | △ or √ | X
Group C | △ | △ | √
CLAP (ours) | √ | √ | √
Group B
Group A
Group C

## Slide 43
Summary
42
Challenges
-MCM designs introduce NUMA effect that can degrade performance
Key Motivations:
- Page size affect NUMA behavior
- Page size sensitivity varies across application
- GPU workloads exhibit strong chiplet-locality
 Solution: CLAP achieves both (1) higher translation efficiency and (2) strong data locality
The key ideas behind CLAP are essential for sustaining performance scalability in emerging MCM GPU designs

## Slide 44
Junhyeok Park Sungbin Jang Osang Kwon Yongho Lee Seokin Hong
Thanks!
Leveraging Chiplet-Locality for Efficient Memory Mapping in Multi-Chip Module GPUs
58th IEEE/ACM International Symposium on Microarchitecture